WEG presents new flexible and efficient geared motors

WEG, a leading global manufacturer of motor and drive technology, is launching the WG20, a new range of highly versatile modular geared motors that offer worldwide interchangeability and up to 96% energy efficiency across a wide range of industrial applications requiring precise and reliable power transmission. The new geared motor will enable users to increase the energy efficiency of systems in their plants significantly, reducing associated energy costs.

Developed in cooperation with the company’s subsidiary – gear technology specialist Watt Drive - the WG20 comes in standardised mounting dimensions to suit both new and existing drive systems, ensuring ease-of-installation and flexibility when retrofitting. It is designed to cover virtually all international supply voltages thanks to internal voltage switching, which makes it easily interchangeable.

Available in energy efficiency classes IE2 and IE3, the motors feature an advanced design, with the pinion directly mounted on to the motor shaft resulting in a two-stage gear unit (in place of the commonly used three-stage unit). Fewer stages means reduced friction, which translates into lower power and heat dissipation and thus more efficiency. Additionally, the improved gear geometry featuring optimised gear teeth and high quality ground gear parts ensure low-loss power transfer and low noise levels, along with reliable performance and extended service life.

“The WG20 - the first WEG-branded geared motor product line – brings together Watt Drive’s high R&D and manufacturing competence and WEG’s motor expertise, which is supported by a global sales and service network,” says Norbert Reisner, Head of Geared Motor Technology at Watt Drive. “By adopting smart design and optimised production processes, we have developed a top-quality geared motor range which fulfils all requirements of modern drive systems across a wide range of industrial applications around the world.”

The compact gear unit design also has a positive impact on the required lubricant volume. The gear arrangement and the advanced housing interior allow the gear units to operate with a low oil level.  The optimised oil fill level and low friction losses in turn prolong the life of the seals and extend the oil change intervals, therefore minimising time and costs associated with maintenance.

The WG20 is built with helical, parallel-shaft and helical bevel gear units with rugged pressure-cast aluminium housings and is suitable for most industrial applications requiring torque ratings between 50 and 600 Nm. International certifications further enhance the geared motor unit’s versatility, enabling users to operate it at 100 or 120 Hz with variable speed drives.

For more information on WEG visit www.weg.net/uk.

Figure captions

WEG000698_Image1: The WG20 product line comprises helical, parallel-shaft and helical bevel geared motors with rugged pressure-cast aluminium housings for rated torques from 50 to 600 Nm

WEG000698_Image2: The intelligent pinion concept allows the WG20 geared motors to cover a wide range of applications with a two-stage configuration

WEG000698_Image3: The rugged pressure-cast aluminium housings developed with the aid of finite-element methods are significantly lighter than previous versions

Follow WEG Europe

## About WEG

WEG is one of the largest global manufacturers of electric equipment, having five main Business Units: Motors, Energy, Transmission and Distribution, Automation and Coatings.  The company employs over 30,000 people worldwide and in 2015 achieved global sales of US$ 3.34 billion, representing success across a wide range of product groups.  These include the latest generation of transformers, LV control gear, generators, gear motors, inverter drive systems, soft starters, LV/MV and HV motors, ATEX-compliant explosion proof motors, smoke extraction motors and full turnkey systems.

Its power generation, transmission and distribution solutions enable those across many industries, especially in the oil & gas, water, power distribution, chemical and petrochemical markets, to operate more efficiently, and to reduce energy usage, carbon emissions and environmental impact. In addition, WEG provides full solutions for renewable energy projects, producing complete wind turbine and solar energy systems.

Editorial Contact

Marco Giudici, Technical Publicity
Tel: +44 (0)1582 390991 
Email: mgiudici@technical-group.com

Company Contact

Marek Lukaszczyk, WEG (UK) Ltd 
Tel: +44(0)1527 513800 Fax: +44(0)1527 513810
Email:  wuk-enquiry@weg.net

## Web: www.weg.net/uk